OPTIMIZATION OF LIVER IRON LOAD ASSESSMENT BY PIXEL-BASED T2* MRI IN THALASSEMIC PATIENTS

A. Shamsakhtari , N Gholizadeh, S Akhlaghpoor, H Soltanianzadeh, MR Fatemizadeh, E Ainaghizadeh, M Nourizadeh, F Daeenejad

1. Department of Nuclear Engineering, Science and Research Branch of Azad University, Tehran, Iran

2. Department of Magnetic Resonance Imaging, Noor Medical Imaging Center, Tehran, Iran

3. Control and Intelligent Processing Center of Excellence (CIPCE), School of Electrical Engineering, College of Engineering, University of Tehran, Iran

4. Image Analysis Laboratory, Department of Radiology, Henry Ford Health System, Detroit, Michigan, USA

5. School of Electrical Engineering, Sharif University of Technology, Tehran, Iran,

6. Cardiology Ward, Dezfool Ganjavian Hospital,Iran, Cardiology Ward, Ahvaz Joundishapoor University

Background: Iron over load is a major problem of treatment in patients with thalassemia.  The accuracy of iron load estimation may suffer from the methodology of T2* measurement.to investigate the precision of different approaches of T2* measurement in order to improve assessment of liver iron load

Methods: 32 â- thallasemic patients (18 male) with the mean age of 20.0±6.5, were involved in this study. A multi-echo fast gradient echo technique on a 1.5T MRI system was used to measure liver iron over load. The T2* map of liver was reconstructed on a pixel-by-pixel basis. The T2* map and MRI image were utilized to determine accurate location of region of interest (ROI). The mean of T2* were computed from the ROIs. The reproducibility of calculated T2* values in two methods was obtained. Moreover, the mean of the pixel’s T2* was calculated in the entire liver parenchyma of one slice. The T2* value of entire slice was compared with the ROI approach.

Results: In the ROI based method, the CoV for the intra-observer reproducibility was 8.5% and for the inter-observer was 9.78%. In the pixel based method, the CoVs for intra-observer and inter-observer reproducibility were 2.79% and 3.91%. There was an acceptable correlation (r=0.96) between the T2* values calculated by the ROI and the entire slice.

Conclusions: The pixel-based approach is more precise to determine the appropriate placement of the ROI. The assessment of T2* in the entire slice reduces the user-based errors significantly.